## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 11

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Appendix E: Passing Arguments into Functions

## Slide 4: Passing Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Three ways to pass arguments (parameters) to functions
  Through registers
  Through memory using references
  Using stack

## Slide 5: Passing Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Passing arguments through registers
  AREA OUR_PROG, CODE, READONLY MOV R0, #5 ; R0 = 5 MOV R1, #7 ; R1 = 7 BL BIGGER ; BIGGER(5, 7) HERE B HERE ; stay here ; ======================================= ; BIGGER returns the bigger value
  ; Parameters: R0 and R1: the values to be compared ; Returns: R0: containing the bigger value ; ======================================= BIGGER CMP R0, R1 BHI L1 ; if R0 > R1 go to L1 MOV R0, R1 ; R0 = R1 L1 BX LR ; return END

## Slide 6: Passing Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Passing through memory using references
  Store the data in memory and pass its address through a register
  ADR R0, OUR_STR ; R0 = addr. of OUR_STR
  BL STR_LENGTH ; STR_LENGTH(&OUR_STR)
  HERE B HERE ; stay here
  OUR_STR DCB "HELLO!"
  ; =======================================
  STR_LENGTH MOV R1, R0 ; move string pointer to R1
  MOV R0, #0 ; use R0 as string length counter
  L_BEGIN LDRB R2, [R1] ; fetch a character from string
  CMP R2, #0
  BXEQ LR ; return if character is null (end of string)
  ADD R1, R1, #1 ; point to next character in string
  ADD R0, R0, #1 ; increment the counter
  B L_BEGIN

## Slide 7: Passing Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Passing arguments through stack
  The arguments are pushed onto the stack just before calling the function and popped off after returning LDR SP, =(0x40000000+(16*1024)) ; init stack pointer
  MOV R0, #5
  PUSH {R0} ; push Arg1
  MOV R0, #7
  PUSH {R0} ; push Arg2
  BL BIGGER ; BIGGER(5, 7)
  ADD SP, SP, #8 ; adjust the stack pointer to remove the arguments
  HERE B HERE ; stay here
  ; =======================================
  BIGGER
  LDR R0, [SP, #4] ; R0 = arg1
  LDR R1, [SP, #0] ; R1 = arg2
  CMP R0, R1
  MOVLO R0, R1 ; if R0 < R1 move R1 into R0
  L1 BX LR ; return

## Slide 8: Passing Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
In ARM CPU, the arguments are passed in the first four registers
  If there are four or fewer arguments
If there are more than four arguments
  The first four are passed in the first four registers
  The rest are passed on the stack

## Slide 9: ARM Application Procedure Call Standard
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
AAPCS provides a standard for implementing the functions
Some rules
  The arguments must be sent through R0 to R3
  The return value must be returned in R0 (and R1 for return a 64-bit)
  The functions can use R4 to R8, R10 and R11 for temporary storage
    Their values must be saved upon entering the function and restored before returning
  The stack must be used as Full Descending

## Slide 10
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
End of Appendix E!