## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 14

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Interrupts (2)

## Slide 4: Interrupts Handling
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Functions to access the NVIC
  void NVIC_EnableIRQ (IRQn_Type IRQn)
  enables the specified device specific interrupt IRQ
  uint32_t NVIC_GetEnableIRQ (IRQn_Type IRQn)
  void NVIC_DisableIRQ (IRQn_Type IRQn)
  void NVIC_SetPendingIRQ (IRQn_Type IRQn)
  uint32_t NVIC_GetPendingIRQ (IRQn_Type IRQn)
  void NVIC_ClearPendingIRQ (IRQn_Type IRQn)
  uint32_t NVIC_GetActive (IRQn_Type IRQn)
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 5: Interrupts Handling
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Functions to access the NVIC
  void NVIC_SetPriority (IRQn_Type IRQn, uint32_t priority)
  The number of priority levels is configurable and depends on the implementation of the chip designer. To determine the number of bits implemented for interrupt priority-level registers, write 0xFF to one of the priority-level register, then read back the value. For example, if the minimum number of 3 bits have been implemented, the read-back value is 0xE0
  Writes to unimplemented bits are ignored
  For Cortex-M3, Cortex-M4, and Cortex-M7
    Dynamic switching of interrupt priority levels is supported
    Supports 0 to 255 priority levels
    Priority-level registers have a maximum width of 8 bits and a minimum of 3 bits
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 6: Interrupts Handling
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Functions to access the NVIC
  uint32_t NVIC_GetPriority (IRQn_Type IRQn)
  uint32_t NVIC_GetVector (IRQn_Type IRQn)
  This function allows to read the address of an interrupt handler function
  void NVIC_SetVector (IRQn_Type IRQn, uint32_t vector)
  This function allows to change the address of an interrupt handler function
  void NVIC_SystemReset (void)
  This function requests a system reset by setting the SYSRESETREQ flag
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 7: Interrupts Handling
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The symbol __Vectors is the address of the vector table in the startup code
Register SCB->VTOR holds the start address of the vector table
SCB: System Control Block, some of its registers:
  ICSR: Interrupt Control and State Register
  VTOR: Vector Table Offset Register
  AIRCR: Application Interrupt and Reset Control Register
  SCR: System Control Register
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 8: Vector Table
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
At the beginning of the vector table, the initial stack value and the exception vectors of the processor are defined
  __Vectors DCD __initial_sp ; Top of Stack initialization
    DCD Reset_Handler ; Reset Handler
    DCD NMI_Handler ; NMI Handler
    DCD HardFault_Handler ; Hard Fault Handler
    DCD MemManage_Handler ; MPU Fault Handler
    DCD BusFault_Handler ; Bus Fault Handler
    DCD UsageFault_Handler ; Usage Fault Handler
    DCD SecureFault_Handler ; Secure Fault Handler
    DCD 0 ; Reserved
    DCD 0 ; Reserved
    DCD 0 ; Reserved
    DCD SVC_Handler ; SVCall Handler
    DCD DebugMon_Handler ; Debug Monitor Handler
    DCD 0 ; Reserved
    DCD PendSV_Handler ; PendSV Handler
    DCD SysTick_Handler ; SysTick Handler
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 9: Vector Table
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Device Specific Vectors
  Following the processor exception vectors, the vector table contains also the device specific interrupt vectors
  __Vectors DCD __initial_sp ; Top of Stack initialization
    DCD Reset_Handler ; Reset Handler
    …
    DCD SysTick_Handler ; SysTick Handler
; device specific interrupts
    DCD WWDG_IRQHandler ; Window Watchdog
    DCD PVD_IRQHandler ; PVD through EXTI Line detect
    DCD TAMPER_IRQHandler ; Tamper
All device specific interrupts should have a default interrupt handler function that can be overwritten in user code
Remapping interrupt vectors by updating VTOR register
  An example: https://www.keil.com/pack/doc/cmsis/Core/html/using_VTOR_pg.html
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 10: interrupt handler function
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
    Default_Handler PROC
    EXPORT WWDG_IRQHandler [WEAK]
    EXPORT PVD_IRQHandler [WEAK]
    EXPORT TAMPER_IRQHandler [WEAK]
    :
    :
    WWDG_IRQHandler
    PVD_IRQHandler
    TAMPER_IRQHandler
    :
    :
    B .
    ENDP
The user application may simply define an interrupt handler function by using the handler name
        void WWDG_IRQHandler(void)
        {
        ...
        }
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 11: interrupt handler function
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
  #include "LPC17xx.h"
  uint32_t active; /* Variable to store interrupt active state */
  void TIMER0_IRQHandler(void) { /* Timer 0 interrupt handler */
    if (LPC_TIM0->IR & (1 << 0)) { /* Check if interrupt for match channel 0 occured */
    LPC_TIM0->IR |= (1 << 0); /* Acknowledge interrupt for match channel 0 occured */
    }
    active = NVIC_GetActive(TIMER0_IRQn); /* Get interrupt active state of timer 0 */
  }
  int main (void) {
    /* Set match channel register MR0 to 1 millisecond */
    LPC_TIM0->MR0 = (((SystemCoreClock / 1000) / 4) - 1); /* 1 ms? */
    LPC_TIM0->MCR = (3 << 0); /* Enable interrupt and reset for match channel MR0 */
    NVIC_EnableIRQ(TIMER0_IRQn); /* Enable NVIC interrupt for timer 0 */
    LPC_TIM0->TCR = (1 << 0); /* Enable timer 0 */
    while(1);
  }
https://www.keil.com/pack/doc/cmsis/Core/html/group__NVIC__gr.html#details

## Slide 12: Masking Exception
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
PRIMASK: Exception mask register (CPU core)
  Register to mask out configurable exceptions
  A 1-bit register
  Setting PRIMASK to 1 raises the execution priority to 0
  CMSIS-CORE API
    void __enable_irq() // clears PM flag
    void __disable_irq() // sets PM flag
    uint32_t __get_PRIMASK() // returns value of PRIMASK
    void __set_PRIMASK(uint32_t x) // sets PRIMASK to x
    BASEPRI: Mask exception from a defined level
      An 8-bit register
      BASEPRI changes the priority level required for exception preemption
      A value of zero disables masking by BASEPRI
    FAULTMASK
      A 1-bit register
      Raises the execution priority to -1 (the priority of HardFault)
      Returning from any exception except NMI clears FAULTMASK to 0
REF: ARMv7-M Architecture Reference Manual

## Slide 13: CMSIS
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
CMSIS: Cortex Microcontroller Software Interface Standard
  Is a vendor-independent hardware abstraction layer for microcontrollers that are based on Arm® Cortex® processors
  Defines generic tool interfaces and enables consistent device support
  Provides simple software interfaces to the processor and the peripherals
  Simplifies software re-use
  Reduces the learning curve for microcontroller developers,
  Reduces the time to market for new devices
Has been created to help the industry in standardization
Enables consistent software layers and device support across a wide range of development tools and microcontrollers
The CMSIS recommends the following conventions for identifiers:
  CAPITAL names to identify Core Registers, Peripheral Registers, and CPU Instructions.
  CamelCase names to identify function names and interrupt functions.
  Namespace_ prefixes avoid clashes with user identifiers and provide functional groups (i.e. for peripherals, RTOS, or DSP Library)
http://www.keil.com/pack/doc/CMSIS/General/html/index.html

## Slide 14: Maximum Interrupt Rate
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
We can only handle so many interrupts per second
  FMax_Int: maximum interrupt frequency
  FCPU: CPU clock frequency
  CISR: Number of cycles ISR takes to execute
  COverhead: Number of cycles of overhead for saving state, vectoring, restoring state, etc.
  FMax_Int = FCPU/(CISR+ COverhead)
  Note that model applies only when there is one interrupt in the system
When processor is responding to interrupts, it isn’t executing our other code
  UInt: Utilization (fraction of processor time) consumed by interrupt processing
  UInt = 100%*FInt* (CISR+COverhead)/ FCPU
  CPU looks like it’s running the other code with CPU clock speed of (1-UInt)*FCPU

## Slide 15: Sharing Data Safely between ISRs and other Threads
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Volatile data: can be updated outside of the program’s immediate control
  In computer programming, particularly in the C, C++, C#, and Java programming languages, the volatile keyword indicates that a value may change between different accesses, even if it does not appear to be modified. This keyword prevents an optimizing compiler from optimizing away subsequent reads or writes and thus incorrectly reusing a stale value or omitting writes. Volatile values primarily arise in hardware access (memory-mapped I/O), where reading from or writing to memory is used to communicate with peripheral devices, and in threading, where a different thread may have modified a value. [Wikipedia]
Non-atomic shared data: can be interrupted partway through read or write, is vulnerable to race conditions

## Slide 16: Non-Atomic Shared Data
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Want to keep track of current time and date
Use 1 Hz interrupt from timer
System
  TimerVal structure tracks time and days since some reference event
  TimerVal’s fields are updated by periodic 1 Hz timer ISR
void GetDateTime(DateTimeType * DT){
DT->day = TimerVal.day;
DT->hour = TimerVal.hour;
DT->minute = TimerVal.minute;
DT->second = TimerVal.second;
}
void DateTimeISR(void){
TimerVal.second++;
if (TimerVal.second > 59){
TimerVal.second = 0;
TimerVal.minute++;
if (TimerVal.minute > 59) {
TimerVal.minute = 0;
TimerVal.hour++;
if (TimerVal.hour > 23) {
TimerVal.hour = 0;
TimerVal.day++;
… etc.
}

## Slide 17: Non-Atomic Shared Data
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Problem
  An interrupt at the wrong time will lead to half-updated data in DT
Failure Case
  TimerVal is {10, 23, 59, 59} (10th day, 23:59:59)
  Task code calls GetDateTime(), which starts copying the TimerVal fields to DT: day = 10, hour = 23
  A timer interrupt occurs, which updates TimerVal to {11, 0, 0, 0}
  GetDateTime() resumes executing, copying the remaining TimerVal fields to DT: minute = 0, second = 0
  DT now has a time stamp of {10, 23, 0, 0}
  The system thinks time just jumped backwards one hour!
Fundamental problem – “race condition”
  Preemption enables ISR to interrupt other code and possibly overwrite data
  Must ensure atomic (indivisible) access to the object

## Slide 18: Examining the Problem More Closely
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Must protect any data object which both
  requires multiple instructions to read or write (non-atomic access),
  and
  is potentially written by an ISR
void GetDateTime(DateTimeType * DT){
uint32_t m;
m = __get_PRIMASK();
__disable_irq();
DT->day = TimerVal.day;
DT->hour = TimerVal.hour;
DT->minute = TimerVal.minute;
DT->second = TimerVal.second;
__set_PRIMASK(m);
}

## Slide 19
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The End (for now)!