## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 16

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
Cortex™-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Serial Peripheral Interface (SPI)

## Slide 4: SPI Description
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Synchronous serial data link
  Provides communication with external devices in Master or Slave Mode
  Is essentially a shift register that serially transmits data bits to other SPIs
  Fast, Easy to use, Simple
A communication protocol using 4 wires
  Also known as a 4 wire bus
Used to communicate across small distances
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 5: SPI Capabilities
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Always Full Duplex
  Communicating in two directions at the same time
Multiple Mbps transmission speed
Transfers data in 8 to 16 bit characters
Multiple slaves
  Daisy-chaining possible
Master controls the data flow
  Other devices act as slaves which have data shifted into and out by the master
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 6: SPI Protocol
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Wires
  Two data lines and two control lines
  Master Out Slave In (MOSI)
    Supplies the output data from the master shifted into the input(s) of the slave(s)
  Master In Slave Out (MISO)
    Supplies the output data from a slave to the input of the master
  Serial Clock (SPCK)
    Is driven by the master and regulates the flow of the data bits. The master may transmit data at a variety of baud rates; the SPCK line cycles once for each bit that is transmitted
  Slave Select (NSS)
    Allows slaves to be turned on and off by hardware
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 7: Embedded Characteristics
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Supports Communication with Serial External Devices
  Four Chip Selects with External Decoder Support Allow Communication with Up to 15 Peripherals
  Serial Memories, such as DataFlash and 3-wire EEPROMs
  Serial Peripherals, such as ADCs, DACs, LCD Controllers, CAN Controllers and Sensors
  External Co-processors
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 8: Block Diagram
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 9: Block Diagram
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 10: Product Dependencies
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
NOTE
  The pins used for interfacing the compliant external devices may be multiplexed with PIO lines. The programmer must first program the PIO controllers to assign the SPI pins to their peripheral functions
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 11: Functional Description
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Modes of Operation: Master and Slave
  Master Mode: MSTR bit = 1 in the Mode Register (SPI_MR)
    The pins NPCS0 to NPCS3 are all configured as outputs
    SPCK pin is driven
    The MISO line is wired on the receiver input
    The MOSI line driven as an output by the transmitter
  Slave Mode: MSTR bit = 0 in the Mode Register (SPI_MR)
    The MISO line is driven by the transmitter output
    The MOSI line is wired on the receiver input
    The SPCK pin is driven by the transmitter to synchronize the receiver
    The NPCS0 pin becomes an input, and is used as a Slave Select signal (NSS)
    The pins NPCS1 to NPCS3 are not driven and can be used for other purposes
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 12: Data Transfer
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Two phases and two polarities of clock
  program clock polarity: CPOL bit in the Chip Select Register
  program clock phase: NCPHA bit
  These two parameters determine the edges of the clock signal on which data is driven and sampled
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 13: SPI User Interface
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 14: SPI Control Register
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Write-only Register
  SPIEN: SPI Enable
  SPIDIS: SPI Disable
  If both SPIEN and SPIDIS are equal to one when the control register is written, the SPI is disabled
  SWRST: SPI Software Reset
    Reset the SPI. A software-triggered hardware reset of the SPI interface is performed
    The SPI is in slave mode after software reset
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 15: SPI Mode Register
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Read-Write Register
  MSTR: Master/Slave Mode
  PS: Peripheral Select
    0 = Fixed Peripheral Select.
    1 = Variable Peripheral Select
  PCSDEC: Chip Select Decode
    0 = The chip selects are directly connected to a peripheral device
    1 = The four chip select lines are connected to a 4- to 16-bit decoder
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 16: SPI Receive Data Register
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Read-Only Register
  RD: Receive Data
    Data received by the SPI Interface is stored in this register right-justified
  PCS: Peripheral Chip Select
    In Master Mode only, these bits indicate the value on the NPCS pins at the end of a transfer
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 17: SPI Transmit Data Register
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Write-Only Register
  TD: Transmit Data
    Data to be transmitted by the SPI Interface is stored in this register
  PCS: Peripheral Chip Select
    This field is only used if Variable Peripheral Select is active
Chapter 32: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 18
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The End (for now)!