## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 17

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
UM10204: I2C-bus specification and user manual, Rev. 6 — 4 April 2014, User manual
ARMv7-M Architecture Reference Manual
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
I2C-bus specification

## Slide 4: I2C Description
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Synchronous serial data link
  Multi-master, multi-slave
  Invented in 1982 by Philips Semiconductor (now NXP Semiconductors)
  Widely used for attaching lower-speed peripheral ICs to processors and microcontrollers in short-distance
  Appropriate for peripherals where simplicity and low manufacturing cost are more important than speed
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 5: I2C Design
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Two bidirectional open collector or open drain lines
  open collector (or open drain): behaves like a switch that is either connected to ground or disconnected
  Serial Data Line (SDA) and Serial Clock Line (SCL)
    pulled up with resistors
7-bit address space (rarely-used 10-bit extension)
Bus speeds
  100 kbit/s: standard mode
  400 kbit/s: Fast mode
  10 kbit/s: low-speed mode
  1 Mbit/s: Fast mode plus
  3.4 Mbit/s: High Speed mode
  5 Mbit/s Ultra Fast-mode
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 6: I2C Design
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Operating roles
  Master: generates the clock and initiates communication with slaves
  Slave: receives the clock and responds when addressed by the master
Multi-master bus: any number of master nodes can be present
Master and slave roles may be changed between messages
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 7: I2C Design
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Potential modes of operation for a given bus device
  Master – master node is sending data to a slave
  Master receive – master node is receiving data from a slave
  Slave transmit – slave node is sending data to the master
  Slave receive – slave node is receiving data from the master
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 8: I2C Data Transfer
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Message delimiters
  START and STOP signals
  Are distinct from the data bits (0 and 1)
The master is initially in master transmit mode by sending a START followed by the 7-bit address of the slave
  followed by a single bit representing whether it wishes to write (0) to or read (1) from the slave
The slave will respond with an ACK bit (active low for acknowledged)
  If slave exists
The address and the data bytes are sent most significant bit first
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 9: I2C Data Transfer
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The start bit is indicated by a high-to-low transition of SDA
  with SCL high
The stop bit is indicated by a low-to-high transition of SDA
  with SCL high
All other transitions of SDA take place with SCL low
To write to the slave
  The Master repeatedly sends a byte with the slave sending an ACK bit
To read from slave
  Master repeatedly receives a byte from the slave, and send an ACK bit after every byte except the last one
https://en.wikipedia.org/wiki/I%C2%B2C

## Slide 10: Two-wire Interface (TWI)
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
I2C-Compatible interface of ATMEL microcontroller
  speeds of up to 400 Kbits/s
Chapter 33: Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 11
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The End (for now)!