## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 21

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Prabal Dutta, “EECS 373 Design of Microprocessor-Based Systems,” University of Michigan
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Sampling, ADCs, and DACs

## Slide 4: We live in an analog world
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Everything in the physical world is an analog signal
  Sound, light, temperature, pressure
Need to convert into electrical signals
  Transducers: converts one type of energy to another
    Electro-mechanical, Photonic, Electrical, …
  Examples
    Microphone/speaker
    Thermocouples
    Accelerometers
EECS 373 Design of Microprocessor-Based Systems

## Slide 5: Transducers
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Transducers convert one form of energy into another
  Allow us to convert physical phenomena to a voltage potential in a well-defined way
EECS 373 Design of Microprocessor-Based Systems
A transducer is a device that converts one type of energy to another. The conversion can be to/from
electrical, electro-mechanical, electromagnetic, photonic, photovoltaic, or any other form of energy.
While the term transducer commonly implies use as a sensor/detector, any device which converts energy can be considered a transducer. [Wikipedia]

## Slide 6: An Example: Photocell
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Convert light to voltage with a CdS Photocell
    Vsignal = (+5V) RR/(R + RR)
  Choose R=RR at median of intended range
  Cadmium Sulfide (CdS)
  tRC = (R+RR)*Cl
    Typically R~50-200kW
    C~20pF
    So, tRC~20-80uS
    fRC ~ 10-50kHz
EECS 373 Design of Microprocessor-Based Systems

## Slide 7: Many other common sensors
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Force
Sound
  Microphones
Position
  Gyros
Acceleration
Field
…
EECS 373 Design of Microprocessor-Based Systems

## Slide 8: Going from Analog to Digital
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
What we want
How we have to get there
EECS 373 Design of Microprocessor-Based Systems
Physical
Phenomena
Engineering Units
Software
Sensor
ADC
Physical
Phenomena
Voltage or
Current
ADC Counts
Engineering Units

## Slide 9: Representing an analog signal digitally
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
How do we represent an analog signal?
  As a time series of discrete values
    On MCU: read the ADC data register periodically
EECS 373 Design of Microprocessor-Based Systems

## Slide 10: Choosing the horizontal range
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
What do the sample values represent?
  Some fraction within the range of values
    What range to use?
EECS 373 Design of Microprocessor-Based Systems
Range Too Small
Range Too Big
Ideal Range

## Slide 11: Choosing the horizontal granularity
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Resolution
  Number of discrete values that represent a range of analog values
  12-bit ADC
    4096 values
    Range / 4096 = Step
Larger range  less information
Quantization Error
  How far off discrete value is
  from actual
  ½ LSB  Range / 8192
Larger range  larger error
EECS 373 Design of Microprocessor-Based Systems

## Slide 12: Choosing the sample rate
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
What sample rate do we need?
  Too little: we can’t reconstruct the signal we care about
  Too much: waste computation, energy, resources
EECS 373 Design of Microprocessor-Based Systems

## Slide 13: Conversion: ADC
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Converting between voltages, ADC counts, and engineering units
  Converting: ADC counts  Voltage
  Converting: Voltage  Engineering Units
EECS 373 Design of Microprocessor-Based Systems

## Slide 14: Conversion: DAC
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
DAC 1: Voltage Divider
EECS 373 Design of Microprocessor-Based Systems

## Slide 15: Conversion: DAC
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
DAC 2: R/2R Ladder
EECS 373 Design of Microprocessor-Based Systems

## Slide 16: ADC in SAM3X
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
A 16-to-1 analog multiplexer
  Making possible the analog-to-digital conversions of 16 analog lines
  The conversions extend from 0V to ADVREF
  supports an 10-bit or 12-bit resolution mode
  conversion results are reported in a common register for all channels
    as well as in a channel-dedicated register
  1 MHz Conversion Rate
  Individual Enable and Disable of Each Channel
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 17: ADC in SAM3X
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Analog-to-Digital Converter Block Diagram
  The temperature sensor is connected to Channel 15 of the ADC
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 18: DAC in SAM3X
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Digital-to-Analog Converter Controller (DACC)
Atmel | SMART ARM-based MCU DATASHEET, SAM3X / SAM3A Series, Atmel-11057C-ATARM-SAM3X-SAM3A-Datasheet_23-Mar-15

## Slide 19
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
The End!