## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 4

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3: Why to Learn Assembly Language
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
HLL can greatly enhance programmer productivity, BUT
Writing assembly code is desirable or necessary for
  The first steps in booting the computer
  Code to handle interrupts
  Low-level locking code for multi-threaded programs
  Code for machines where no compiler exists
  Code which needs to be optimized beyond the limits of the compiler
  On computers with very limited memory
  Code that requires low-level access to architectural and/or processor features
  Write a compiler
  Program device drivers

## Slide 4
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
ARM Architecture and Assembly Language Programming

## Slide 5: SUB Instruction
We have already seen MOV and ADD instr.
SUB Rd, Rn, Op2 ; Rd = Rn – Op2
A simple code
MOV R1, #0x34 ; load 0x34 into R1 (R1 = 0x34) SUB R5, R1, #0x25 ; R5 = R1 – 0x25 (R5 = 0x34 – 0x25)
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 6: ALU Instructions Using GPRs
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 7: The ARM Memory Map
Memory space allocation in the ARM
  4 gigabytes of directly accessible memory space
    from 0 to 0xFFFFFFFF
Memory space can be divided into five sections
  On-chip peripheral and I/O registers
  On-chip data SRAM
  On-chip EEPROM (for saving critical data)
  On-chip Flash ROM (program space)
  Off-chip DRAM space
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 8: The ARM Memory Map
Why both EEPROM and Flash?
Why both SRAM and EEPROM?
IO-mapped or Memory-Mapped IO?
Memory space is 4GB; is it enough?
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 9: The ARM Memory Map
Q: A given ARM chip has the following address assignments. Calculate the space and the amount of memory given to each section.
(a) Address range of 0x00100000 – 0x00100FFF for EEPROM
  (b) Address range of 0x40000000 – 0x40007FFF for SRAM
  (c) Address range of 0x00000000 – 0x0007FFFF for Flash
  (d) Address range of 0xFFFC0000 – 0xFFFFFFFF for peripherals
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
peripherals

## Slide 10: Load and Store Instructions
Load Rd with the contents of location pointed to by Rx register
LDR Rd,[Rx]; Rx contains an address between 0x00000000 to 0xFFFFFFFF
LDR reads one word (32-bit or 4-byte) of data
  from 4 consecutive memory locations
  The locations can be in the SRAM, a Flash memory or I/O registers
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 11: Load and Store Instructions
Store register Rd into locations pointed to by Rx
STR Rd,[Rx]
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 12: Load and Store Variations
Load a byte
LDRB Rd, [Rx]
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 13: Load and Store Variations
Store a byte
STRB Rd, [Rx]
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 14: Load and Store Variations
Load half-word (2-byte)
LDRH Rd, [Rx]
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 15: Load and Store Variations
Store half-word (2-byte)
STRH Rd, [Rx]
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 16: Current Program Status Register
CPSR: Flag register
N: Negative
Z: Zero
C: Carry
V: Overflow
T: Thumb
I and F: enable or disable the interrupt
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 17: S suffix and the status register
By executing data processing instructions
  By default, the status flags of CPSR are not updated
To Update the flags
  put the ‘S’ suffix at the end of the opcode
  ADD => ADDS
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 18: S Suffix and the Status Register
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 19: Flag Bits and Decision Making
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Conditional branch instructions

## Slide 20
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
ARM Data Format, Pseudo-instructions and Directives

## Slide 21: ARM Data Format
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Data format representation
  Hexadecimal numbers
  MOV R1, #0x99
  Decimal numbers
  MOV R7, #12
  Binary numbers
  MOV R6, #2_10011001
  Numbers in any base between 2 and 9
  MOV R7, #8_33
  ASCII characters
  LDR R3, #'2' ; R3 = 00110010 or 32 in hex

## Slide 22: Pseudo-instructions
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
LDR pseudo-instruction
  Limitation of loading immediate value: 8-bit
    MOV Rd, 0x11223344
    LDR Rd, =32-bit_immediate_value
    LDR R7, =0x11223344
Load registers with the addresses of memory locations
    ADR Rn, label

## Slide 23: Assembler Directives
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Directives give directions to the assembler
  Some Widely Used ARM Directive

## Slide 24: Assembler Directives
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Directives: AREA
  Defines a new section of memory
  AREA sectionname, attribute, attribute, ...
  Some attributes: CODE, DATA, READONLY, READWRITE, and ALIGN
  AREA MY_ASM_PROG1, CODE, READONLY

## Slide 25: Assembler Directives
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Directives: AREA
  Attributes: READONLY
    All the READONLY sections of the same program are put next to each other in the flash memory by the linker
  Attributes: READWRITE
    The linker puts all the READWRITE sections of the same program next to each other in the SRAM memory
  Attributes: CODE: is by default READONLY memory
  Attributes: DATA: is by default READWRITE memory
  Attributes: ALIGN: to align a section

## Slide 26: Assembler Directives
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Directives: END
  Indicates to the assembler the end of the source code
  Is the last line of the ARM assembly program
    Anything after the END directive in the source file is ignored by the assembler
        AREA PROG_2_1, CODE, READONLY MOV R1, #0x25 ; R1 = 0x25 MOV R2, #0x34 ; R2 = 0x34 ADD R3, R2, R1 ; R3 = R2 + R1
    HERE B HERE ; stay here forever
      END

## Slide 27: Assembler Directives
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Directives: END
  Indicates to the assembler the end of the source code
  Is the last line of the ARM assembly program
    Anything after the END directive in the source file is ignored by the assembler
        AREA PROG_2_1, CODE, READONLY MOV R1, #0x25 ; R1 = 0x25 MOV R2, #0x34 ; R2 = 0x34 ADD R3, R2, R1 ; R3 = R2 + R1
    HERE B HERE ; stay here forever
      END