## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 6

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Arithmetic and Logic Instructions and Programs

## Slide 4: Arith. Instr. and Flag Bits for Unsigned Data
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
No increment instr. In ARM
  Use the available ADD instr.

## Slide 5: Multiword ADD and SUB
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Add 0x35F62562FA to 0x21F412963B
      LDR R0, =0xF62562FA; R0 = 0xF62562FA
      LDR R1, =0xF412963B; R1 = 0xF412963B
      MOV R2, #0x35; R2 = 0x35
      MOV R3, #0x21; R3 = 0x21
      ADDS R5, R1, R0; R5 = 0xF62562FA + 0xF412963B ; now C = 1
      ADC R6, R2, R3; R6 = R2 + R3 + C; = 0x35 + 21 + 1 = 0x57

## Slide 6: Multiword ADD and SUB
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Sub 0x21F62562FA from 0x35F412963B
      LDR R0, =0xF62562FA; R0 = 0xF62562FA ; notice the syntax for LDR
      LDR R1, =0xF412963B; R1 = 0xF412963B
      MOV R2, #0x21; R2 = 0x21
      MOV R3, #0x35; R3 = 0x35
      SUBS R5, R1, R0; R5 = R1 – R0; = 0xF412963B – 0xF62562FA, and C = 0
      SBC R6, R3, R2; R6 = R3 – R2 – 1 + C; = 0x35 – 0x21 – 1 + 0 = 0x13

## Slide 7: Multiplication and Division of Unsigned Numbers
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Not all CPUs have instr. for mult. and div.
  All the ARM processors have mult., but not all have div.
  ARM Cortex-M3 and M4 have both mult. and div.
MUL: Regular multiplication
MULL: long multiplication

## Slide 8: Multiplication of Unsigned Numbers
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
MUL: Regular multiplication
MULL: long multiplication
    LDR R1, =100000; R1=100,000
    LDR R2, =150000; R2=150,000
    MUL R3, R2, R1; R3 is not 15,000,000,000; it cannot fit in 32 bits.
    LDR R1, =0x54000000; R1 = 0x54000000
    LDR R2, =0x10000002; R2 = 0x10000002
    UMULL R3, R4, R2, R1; 0x54000000 × 0x10000002 = 0x054000000A8000000; R3 = 0xA8000000, the lower 32 bits
    ; R4 = 0x05400000, the higher 32 bits

## Slide 9: Multiplication of Unsigned Numbers
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Multiply and Accumulate Instructions in ARM
    MLA Rd, Rm, Rs, Rn ; Rd = Rm × Rs + Rn
    MOV R1, #100; R1 = 100
    MOV R2, #5; R2 = 5
    MOV R3, #40; R3 = 40
    MLA R4, R1, R2, R3; R4 = R1 × R2 + R3 = 100 × 5 + 40 = 540
To accumulate the products of the multiplication
    MLA R3, R1, R2, R3; R3 = R1 × R2 + R3 or R3 += R1 × R2
UMLAL: unsigned multiply and accumulate long
    UMLAL RdLo, RdHi, Rn, Op2; RdHi:RdLo = Rn × Op2 + RdHi:RdLo

## Slide 10: Rotate and Barrel Shifter
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
LSR: Logical shift right
    MOV R0, #0x9A; R0 = 0x9A
    MOVS R1, R0, LSR #3; shiftR R0 3 times, then store the result in R1
    MOV R0, #0x9A
    MOV R2, #0x03
    MOVS R1, R0, LSR R2; shiftR R0 R2 times; and move the result to R1

## Slide 11: Rotate and Barrel Shifter
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
LSL: Logical shift left
    MOV R1, R1, LSL R2
ROR: Rotate right
    MOVS R1, R1, ROR #1
    MOVS R1, R1, ROR R0

## Slide 12: Rotate and Barrel Shifter
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
NO ROL: Rotate left
  Use ROR for rotating left
  n-bit ROL  (32 - n)-bit ROR
    Take care of carry
RRX: Rotate right through carry
  Takes no arguments
    MOVS R2, R2, RRX; Rotate 1 bit

## Slide 13: Rotating Immediate Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
MOV Instruction
MOV R0, #0xFF, #2; R0 = 0xFF is rotated right 2 times. R0 = 0xC000003F
MOV R0, #0xFF, #12; R0 = 0xFF is rotated right 12 times. R0 = 0x0FF00000
MOV R0, #0xFF, #28; R0 = 0xFF is rotated right 28 times. R0 = 0x00000FF0
BUT, Rotate field (bit11-bit8) is 4-bit

## Slide 14: Rotating Immediate Arguments
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Shift instruction
MOV R0, R2, LSL #8  LSL R0, R2, #8
ASR: Arithmetic Shift right
ASR Rd, Rm, Rn
ASRS Rd, Rm, Rn
LSL: Logical Shift Left
LSL Rd, Rm, Rn
…

## Slide 15: BCD and ASCII Conversion
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Unpacked BCD: each decimal digit is represented by a byte
0000 1001 0000 0101  95
Packed BCD: two decimal digits are packed in one byte
1001 0101  95
ASCII to unpacked BCD conversion
  Get rid of the "011" in the upper 3 bits of the 7-bit ASCII
    ASCII number is ANDed with "0000 1111“
ASCII to packed BCD conversion
  First convert to unpacked BCD (remove the upper 3 bits)
  Combine every two digits to make a packed BCD

## Slide 16: BCD and ASCII Conversion
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Packed BCD to ASCII conversion
  Convert packed BCD to unpacked BCD
  Tagged with 011 0000 (0x30)

## Slide 17
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
End of Chapter 3!