## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 8

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Signed Integer Numbers Arithmetic

## Slide 4: Signed number
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Sign extension and avoiding erroneous results
    ; assume memory location 0x80000 has +96 = 0110 0000 and R1=0x80000
    LDRSB R0, [R1] ; now R0 = 00000000000000000000000001100000
    ; assume memory location 0x80000 contains -2 = 1111 1110 and R2=0x80000
    LDRSB R4, [R2] ; now R4 = 11111111111111111111111111111110
    ; assume 0x80000 contains +260 = 0000 0001 0000 0100 and R1=0x80000
    LDRSH R0, [R1] ; R0=0000 0000 0000 0000 0000 0001 0000 0100
    ; assume location 0x20000 has -327660=0x8002 and R2=0x20000
    LDRSH R1, [R2] ; R1=FFFF8002

## Slide 5: Signed number
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Signed number multiplication: SMULL
    LDR R1, =-3500 ; R1 = -3500 (0xFFFFF254)
    LDR R0, =-100 ; R0 = -100 (0xFFFFFF9C)
    SMULL R2, R3, R0, R1
Signed number comparison
    CMP Rn, Op2
    Op2 > Rn V = N Op2 = Rn Z = 1 Op2 < Rn N ≠ V

## Slide 6: Arithmetic Shift
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
ASR (arithmetic shift right)
    MOV Rn, Op2, ASR count
    or
    ASR Rn, Op2, count

## Slide 7
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
End of Chapter 5!