## Slide 1: Microprocessors and Assembly Language Fall 2019
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
Lecture 9

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran

## Slide 3
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
ARM Memory Map, Memory Access, and
Stack

## Slide 4: Memory Addressing
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Memory Byte Addressing in ARM

## Slide 5: Memory Addressing
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Sample Memory Space Allocation in ARM

## Slide 6: AHB and APB buses
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
AHB: advanced high-performance bus
  Connects CPU to RAM, ROM, …
APB: advanced peripherals bus
  Dedicated for communication with the on-chip peripherals
    timers, ADC, UART, SPI, I2C, …

## Slide 7: Data Misalignment in SRAM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Compilers make sure that instructions are always aligned
Placement of data in SRAM can be nonaligned
  Memory access penalty

## Slide 8: Data Misalignment in SRAM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
    LDR R1, =0x40000000 ; R1=0x40000000
    LDR R2, =0x4598F31E ; R2=0x4598F31E
    STR R2, [R1] ; Store R2 to location 0x40000000
    ADD R1, R1, #1 ; R1 = R1 + 1 = 0x40000001
    STR R2, [R1] ; Store R2 to location 0x40000001

## Slide 9: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Base plus offset addressing modes
  Pre-indexed addressing mode with fixed offset
    LDR R5, =0x55667788
    LDR R1, =0x10000000; load the address of first location
    STR R5, [R1] ; store R5 to location 0x10000000
    STR R5, [R1, #4]; store R5 to location 0x10000000 + 4 (0x10000004)
    STR R5, [R1, #8]; store R5 to location 0x10000000 + 8 (0x10000008)
    STR R5, [R1, #0x0C]; store R5 to location 0x10000000 + 0x0C (0x1000000C)

## Slide 10: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Base plus offset addressing modes
      Pre-indexed addressing mode with writeback and fixed offset
        The calculated pointer is written back to the pointing register
        LDR R1, =0x10000000 ; load the address of first location
        STR R5, [R1] ; store R5 to location 0x10000000
        STR R5, [R1, #4]!; store R5 to location 0x10000000 + 4 (0x10000004)
        ; writeback makes R1 = 0x10000004
        STR R5, [R1, #4]!; store R5 to location 0x10000004 + 4 (0x10000008)
        ; writeback makes R1 = 0x10000008
        STR R5, [R1, #4]!; store R5 to location 0x10000008 + 4 (0x1000000C)
        ; writeback makes R1 = 0x1000000C

## Slide 11: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Base plus offset addressing modes
      Post-indexed addressing mode with fixed offset
        Update pointer after the load/store operation
        STR R1, [R2], #4 ; store R1 into memory pointed to by R2 and then write back R2 + 4 to R2
        LDRB R5, [R3], #1 ; load a byte from memory pointed to by R3 and then write back R3 + 1 to R3

## Slide 12: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Pre-indexed address mode with offset of a shifted register
      Simple format
        LDR Rd, [Rm, Rn] ; Rd is loaded from location Rm + Rn of memory
        STR Rs, [Rm, Rn] ; Rs is stored to location Rm + Rn of memory
      General format
        LDR Rd, [Rm, Rn, <shift>] ; (Shifted Rn) + Rm is used as the address
        STR Rd, [Rm, Rn, <shift>] ; (Shifted Rn) + Rm is used as the address
        LDR R1, [R2, R3, LSL #2] ; R2 + (R3 × 4) is used as the address
        STR R1, [R2, R3, LSL #1] ; R2 + (R3 × 2) is used as the address
        STRB R1, [R2, R3, LSL #2] ; R2 + (R3 × 4) is used as the address
        ; least significant byte of R1 is stored at location R2 + (R3 × 4)
        LDR R1, [R2, R3, LSR #2] ; R2 + (R3 / 4) is used as the address

## Slide 13: Advanced Indexed Addressing Mode
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Writeback sign (!) in pre-indexed ld/st with scaled register
        LDR R1, [R2, R3, LSL #2]!; R2 + (R3 × 4) is used as the address,
            ; content of location R2 + (R3 × 4) is loaded to R1
            ; R2 = R2 + (R3 × 4) (R2 is updated.)
        STR R1, [R2, R3, LSL #1]!; R2 + (R3 × 2) is used as the address
                ; R1 is stored to location R2 + (R3 × 2)
            ; R2 = R2 + (R3 × 2) (R2 is updated)
    Scaled register post-indexed
        STR R1, [R2], R3, LSL #2; store R1 at location R2 of memory ; and write back R2 + (R3 × 4) to R2. LDR R1, [R2], R3, LSL #2; load location R2 of memory to R1 ; and write back R2 + (R3 × 4) to R2

## Slide 14: Stack and Stack Usage in ARM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Stack: A data structure that allows easy access to the top of the stack
Stack in assembly: A section of memory to store data temporarily
  Hardware support to facilitate the creation and maintenance of stack
All the general registers can be used as a stack pointer
Descending stack: pointing to a lower address after push
Ascending stack: pointing to a higher address after push
Empty stack: point to where the new data will be stored
Full Stack: point to where the old data will be taken off
instructions PUSH, POP and interrupt handling assume the stack to be full descending

## Slide 15: Stack and Stack Usage in ARM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Full descending stack
  Stack pointer is pointing to the last word of data put onto the stack
If the stack is empty (no data stored in the stack yet)
  SP is pointing to the word immediately below the stack
Initializing the stack pointer in ARM
  The R13 (SP) register contains value 0 at power up
  We must initialize the SP at the beginning of the program
    Point to somewhere in the internal SRAM

## Slide 16: Stack and Stack Usage in ARM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Stack_Top equ 0x40008000
AREA EXAMPLE_6_17, CODE, READONLY
LDR R13, =Stack_Top ; load SP
LDR R0, =0x125 ; R0 = 0x125
LDR R1, =0x144 ; R1 = 0x144
MOV R2, #0x56 ; R2 = 0x56
BL MY_SUB ; call a subroutine
ADD R3, R0, R1
ADD R3, R3, R2
HERE B HERE ; stay here
MY_SUB
; save R0, R1, and R2 on stack before use
SUB R13, R13, #4
STR R0, [R13] ; save R0 on stack
SUB R13, R13, #4
STR R1, [R13] ; save R1 on stack
SUB R13, R13, #4
STR R2, [R13] ; save R2 on stack
; -------- modify R0, R1, and R2
MOV R0, #15
MOV R1, #25
SUB R2, R0, R1
STR R2, [LR, #4]
; restore the original registers contents from stack
LDR R2, [R13] ; restore R2 from stack
ADD R13, R13, #4 ; R13 = R13 + 4 to increment the stack pointer
LDR R1, [R13] ; restore R1 from stack
ADD R13, R13, #4 ;
LDR R0, [R13] ; restore R0 from stack
ADD R13, R13, #4
BX LR ; return to caller
END

## Slide 17: Stack and Stack Usage in ARM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
STM and LDM
  To store and load multiple registers with a single instruction
    MY_SUB
    ; --------save R0, R1, and R2 on stack before they are used by a loop
    STMFA R13, {R0-R2} ; save R0, R1, R2 on stack using Full Ascending
    ; --------R0, R1, and R2 are changed
    MOV R0, #0 ; R0=0
    MOV R1, #0 ; R1=0
    MOV R2, #0 ; R2=0
    ; ---------restore the original registers contents from stack
    LDMFA R13, {R0-R2}
    ; restore R0, R1, and R2 from stack using Full Ascending
    BX LR ; return to caller

## Slide 18: Stack and Stack Usage in ARM
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Options for LDM and STM instructions
PUSH is an alias of “STMDB R13!”
POP is an alias of “LDMIA R13!”

## Slide 19: Subroutine Call
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Stack frame
  A block of memory on the stack for a subroutine
  Parameters are pushed onto the stack by the caller
  The return address is pushed onto the stack from R14
Subroutine moves the stack pointer to leave a block of memory space for the local variables
The stack pointer is copied to another register to be used for access into the stack frame
Each subroutine should preserve any register it is going to use and restore them before return

## Slide 20: ARM Bit-Addressable Memory Region
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Bit-banding option
  Generally available in M3 and M4
  To mitigate the issues of Read-Modify-Write
  Only few small regions are bit-banded

## Slide 21: ARM Bit-Addressable Memory Region
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
A program to set HIGH the D6 of the SRAM location 0x20000001
  LDR R1, =0x20000001 ; load the address of the byte
  LDRB R2, [R1] ; get the byte
  ORR R2, R2, #2_01000000 ; make D6 bit high
  ; (binary representation in Keil for 0b01000000)
  STRB R2, [R1] ; write it back
  LDR R1, =0x22000038 ; load the alias address of the bit MOV R2, #1 ; R2 = 1 STR R2, [R1] ; Write one to D6

## Slide 22: ADR, LDR, and PC Relative Addressing
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
Using PC (R15) register as the pointer register
  LDR R0, [PC, #4]
What is the value of R0 if LDR is in address 0x00000004?
R0= 0x00000004 + 4 + 8
  The ADR Pseudo-instruction
  ADR Rn, Label  ADD Rn, PC, #offset
  Implementing the LDR Pseudo-instruction
  LDR R2, =0x12345678
  Assembler stores the value as a constant in program memory
    LDR R2, [PC, #0x0008]

## Slide 23
Microprocessors and Assembly Language, Fall 2019, AUT, Tehran, Iran
End of Chapter 6!